LOYOLA COLLEGE (AUTONOMOUS), CHENNAI – 600 034

B.Sc. DEGREE EXAMINATION – PHYSICS

THIRD SEMESTER – APRIL 2011

# PH 3504/PH 3502/PH 5501 - ELECTRONICS - I

Date : 12-04-2011 	Dept. No.	                                                   Max. : 100 Marks

Time : 1:00 - 4:00

# PART – A

Answer ALL questions.                                                                        		 (10 x 2 = 20 marks)

1. State Norton’s theorem.

2. State the conditions for oscillations in an Oscillator.

3. Define β. Show that β= α/ (1-α)

4. For an inverting amplifier using Op-Amp, R1=1K and Rf = 10 K. Assuming the  
    amplifier to be ideal, calculate the output voltage for an input of 1V.

5. Define CMRR.

6. What is don’t care condition in K- map?

7. Construct the K-map for a 4-variable truth table in which the output is high for the  
    following input conditions ABCD = 1101, 1010, 0101, 1111

8. What is a Multiplexer?

9. The terminal count of a MOD 13 binary counter is________ a)1111   b) 1101 c) 1100  
     d) 0100

10. A 4-bit asynchronous counter uses Flip-Flops of propagation delay time 20 ns each.  
      The maximum possible time required for change of state is  _________

a)60 ns   b) 20 ns   c)80 ns   d)40ns

PART - B

Answer ANY FOUR questions.                                                          		  (4 x 7.5 = 30 marks)

11.a)  Derive the condition for transfer of maximum power from a source to a load. (4)

b) A generator develops 200 V and has an internal resistance of 100 Ω. Find the  
          power delivered to a load of 100 Ω. What is the efficiency?  (3.5)

12. With a neat diagram, explain the construction and working of a phase shift oscillator.

13. Derive expressions for the gain of inverting and non-inverting amplifiers using Op- 
      Amp.												(3+4.5)

14. Draw the logic circuit of a Master- Slave flip-flop and explain its working. How is the   
     race around problem overcome?

15. Explain with theory, the working of MOD7 asynchronous UP counter.

PART - C

Answer ANY FOUR questions.                                                       			 (4 x 12.5 = 50 marks)

16. Give the equivalent circuit of a CE amplifier using h- parameters. Hence derive expressions for Ai, Av    and Zi in terms of h-parameters.  									(4+8.5)

17. a) Explain the construction and working of Bistable Multivibrator with a neat diagram.

b) A  potential divider circuit has the following values. IE = 2mA, IB = 50 µA , VBE =  
          0.2 V, RE= 1 k and R2 = 10 k and VCC = 10V. Find the value of R1.  				(8+4.5)

18. a) Explain the working of averaging amplifier using Op-Amp.

b) Solve the given simultaneous equations using Op-Amps.

2  X  +   3Y =  14  and  2 X  – Y  = 4         							(5+7.5)

19. Simplify the Boolean function

F(A,B,C,D)   =  Σm (  1,3,7,11,15)  + Σd  (0,2,5 )

Implement the simplified expression as a logic diagram with only two input NAND  
      gates only.   											(6+6.5)

20. Write detailed notes on:

a) Shift registers	b) Read Only Memory and 	c) Random Access Memory.	         (4.5+4+4)

SSSSSSS