LOYOLA COLLEGE (AUTONOMOUS), CHENNAI – 600 034

M.Sc. DEGREE EXAMINATION – STATISTICS

FOURTH SEMESTER – April 2009

# ST 4808 - STATISTICAL COMPUTING - III

Date & Time: 25/04/2009 / 9:00 - 12:00  Dept. No. 	                                                   Max. : 100 Marks

Answer any three questions

- a)  The data shown here are  and R values for 24 samples of size n=5 taken from a process producing bearings.  The measurements are made on the inside diameter of the bearing, with only the last three digits recorded.

| Sample number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 34.5 | 34.2 | 31.6 | 31.5 | 35.0 | 34.1 | 32.6 | 33.8 | 34.8 | 33.6 | 31.9 |
| R | 3 | 4 | 4 | 4 | 5 | 6 | 4 | 3 | 7 | 8 | 3 |
| Sample number | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 |
|  | 38.6 | 35.4 | 34 | 37.1 | 34.9 | 33.5 | 31.7 | 34 | 35.1 | 33.7 | 32.8 |
| R | 9 | 8 | 6 | 5 | 7 | 4 | 3 | 8 | 4 | 2 | 1 |
| Sample number | 23 | 24 |  |  |  |  |  |  |  |  |  |
|  | 33.5 | 34.2 |  |  |  |  |  |  |  |  |  |
| R | 3 | 2 |  |  |  |  |  |  |  |  |  |

(i). Sep up  and R charts on this process.  Does the process seem to be in statistical           control?  If necessary, revise the trial control limits.

(ii). If specifications on this diameter are 0.50300.0010, find the percentage of nonconforming bearings produced by this process.  Assume that diameter is normally distributed.

b). In the semiconductor industry, the production of microcircuits involves many steps.  The wafer fabrication process typically builds these microcircuits on silicon wafers and there are many microcircuits per wafer.  Each production lot consists of between 16 and 48 wafers.  Some processing steps treat each wafer separately, so that the batch size for that step is one wafer.  It is usually necessary to estimate several components of variation: within-wafer, between-wafer, between-lot and the total variation. A critical dimension (measured in mm) is of interest to the process engineer. Suppose that five fixed position are used on each wafer (position 1 is the center) and that two consecutive wafers are selected of each batch. The data that results several batches are shown below.

(i) What can you say about over all process capability?

(ii)  Can you construct control charts that allow within- wafer variability to be evaluated?

(iii) What control charts would you establish to evaluate variability between wafers? Set

up these charts and use them to draw conclusions about the process.

| Lot No. | Wafer No. | Position |
| --- | --- | --- |
|  |  | 1 | 2 | 3 | 4 | 5 |
| 1 | 1 | 2.15 | 2.13 | 2.08 | 2.12 | 2.10 |
|  | 2 | 2.13 | 2.10 | 2.04 | 2.08 | 2.05 |
| 2 | 1 | 2.02 | 2.01 | 2.06 | 2.05 | 2.08 |
|  | 2 | 2.03 | 2.09 | 2.07 | 2.06 | 2.04 |
| 3 | 1 | 2.13 | 2.12 | 2.10 | 2.11 | 2.08 |
|  | 2 | 2.03 | 2.08 | 2.03 | 2.09 | 2.07 |
| 4 | 1 | 2.04 | 2.01 | 2.10 | 2.11 | 2.09 |
|  | 2 | 2.07 | 2.14 | 2.12 | 2.08 | 2.09 |
| 5 | 1 | 2.16 | 2.17 | 2.13 | 2.18 | 2.10 |
|  | 2 | 2.17 | 2.13 | 2.10 | 2.09 | 2.13 |
| 6 | 1 | 2.04 | 2.06 | 2.00 | 2.10 | 2.08 |
|  | 2 | 2.03 | 2.10 | 2.05 | 2.07 | 2.04 |
| 7 | 1 | 2.04 | 2.02 | 2.01 | 2.00 | 2.05 |
|  | 2 | 2.06 | 2.04 | 2.03 | 2.08 | 2.10 |
| 8 | 1 | 2.13 | 2.10 | 2.10 | 2.15 | 2.13 |
|  | 2 | 2.10 | 2.09 | 2.13 | 2.14 | 2.11 |
| 9 | 1 | 2.00 | 2.03 | 2.08 | 2.07 | 2.08 |
|  | 2 | 2.01 | 2.03 | 2.06 | 2.05 | 2.04 |
| 10 | 1 | 2.04 | 2.08 | 2.09 | 2.10 | 2.01 |
|  | 2 | 2.06 | 2.04 | 2.07 | 2.04 | 2.01 |

(17 +17)

- a). Bath concentrations are measured hourly in a chemical process.  Data (in PPM) for the

last 32 hours are shown below (read down from left).

| 160 | 186 | 190 | 206 |
| --- | --- | --- | --- |
| 158 | 195 | 189 | 210 |
| 150 | 179 | 185 | 216 |
| 151 | 184 | 182 | 212 |
| 153 | 175 | 181 | 211 |
| 154 | 192 | 180 | 202 |
| 158 | 186 | 183 | 205 |
| 162 | 197 | 186 | 197 |

The process target is =175 PPM.

(i). Estimate the process standard deviation.

(ii). Construct a tabular cusum for this process using standardized values of h = 5 and

k =  .

b). A product is shipped in lots of size N = 2000.  Find a Dodge-Romig single-sampling plan for which the LTPD = 1%, assuming that the process average is 0.25% defective.  Draw the OC curve and ATI curve for this plan.  What is the AOQL for this sampling plan?									         			(20+14)

3)    (a)  Analyze the following 32 factorial design						(24)

Replicate I           			 Replicate II

| a0b0 20 | a1b0 32 | a0b2 40 |
| --- | --- | --- |
| a1b1 60 | a0b1 48 | a2b0 55 |
| a2b1 60 | a1b2 31 | a2b2 51 |
| a1b1 42 | a1b2 60 | a0b1 40 |
| a2b0 25 | a0b0 62 | a1b0 45 |
| a2b2 61 | a2b1 31 | a0b2 42 |

(b) Construct BIBD using the following :

V = 7, b =7, r = 3, k = 3, λ=1 							    (10)

4)  (a) Analyze the following 23 factorial experiment in blocks of 4 plots, involving three fertilizers N,

P and K each at two levels.								(17)

Replicate I		Replicate II

| Block 1 | np 88 | npk 90 | (1) 115 | k 75 |
| --- | --- | --- | --- | --- |
| Block 2 | p 101 | n 111 | pk 75 | nk 55 |
| Block 3 | (1) 115 | npk 95 | nk 90 | p 80 |
| Block 4 | np 125 | k 95 | pk 80 | n 100 |

Replicate III

| Block 5 | pk 53 | nk 76 | (1) 65 | np 82 |
| --- | --- | --- | --- | --- |
| Block 6 | n 75 | npk 100 | P 55 | k 92 |

(b) Use the Kuhn-Tucker conditions to solve the following Non-Linear Programming Problem:

Maximize z =  2x1 + x2 -x12

Subject to the constraints:

2x1+ 3x2 ≤ 6,

5x1+ 2x2 ≤ 10

x1, x2 ≥ 0							(17)

5)  (a)  Use Penalty method to solve the following L.P.P:

Minimize = 9x1 + 10x2

Subject to the constraints:

2x1 + 4x2  ≥ 50,

4x1 + 3x2  ≥ 24,

3x1 + 2x2   ≥ 60

x1, x2 ≥ 0									(17)

(b)   Use Beale’s method to solve the following Q.P.P:

Minimize z = 6- 6x1 + 2x12 – 2x1x2 + 2x22

Subject to x1 + x2 ≤ 2

x1, x2 ≥ 0							(17)

**************

# Text boxes

YB 50